## Slide 1: BioSAXS
Documentation
Alejandro de Maria Antolinos
28/03/2012

## Slide 2: Index
Samples. List of terms related to samples
Data Acquisition. List of terms related to data Acquisition
Use cases
Sample Changer
ISPYB – BsxCube Interface

## Slide 3: SAMPLES

## Slide 4: List of terms related to samples
ABC
A*C*
A*B*
C*
D*
A*
assembly ‘X’
= Macromolecule
= assembly
Biological assembly
for investigation
A macromolecule is a biological construct
In solution for investigation
Description of an assembly containing
multiple macromolecules
It could be in rare cases more then one assembly the macromolecule belongs to so we should be careful of how to describe
this and or strict with the definition
E*
B*
EBD
assembly ‘Y’

## Slide 5: List of terms related to samples
= Macromolecule: biological construct in solution for investigation
= assembly: Description of an assembly containing multiple macromolecules
Acronym
Molecular Mass
Number of individual protein chain and residues in each
Number of individual DNA strands and bases in each
Number of individual RNA strands and bases in each
Sequence
assembly (s)
  List of regions indicating which part of the assembly(s) the macromolecule is
List of possible structures (PDB)
  Which part of the macromolecule the structure is
Macromolecule
List of macromolecules

## Slide 6: List of terms related to samples
= Sample: Specific measurement details for the macromolecule
Macromolecule
Buffer
Concentration > 0
Temperature
  Set Point
  Measure for each frame
Name: MACROMOLECULE acronym_BUFFER acronym_CONCENTRATION ???
Type of measurement
Volume to load
Comments
= Buffer: the matched solution in which a sample is suspended
Name/Acronym
Concentration = 0
Temperature
  Set Point
  Measure for each frame
Type of measurement
Volume to load
pH
Composition
List of additives

## Slide 7: List of terms related to samples
= Additive: Any component of the buffer which will be varied in an experiment (salts, ligands, detergents, lipids, deuteration)
= Structure
Name
Quantity
Type
Buffer
A PDB file or accession code
List of what data this structure is associated with
  assembly
    Macromolecule

## Slide 9: Visual Data Model Draft for Assembly
A assembly has 1..N macromolecules
A macromolecule has 0..N samples
A sample has 1 buffer associated
A buffer has 0..N additives
macromolecule
assembly
Sample: macromolecule + buffer
Additives
………
1
N
………
N
N
1
1

## Slide 10: Data Acquisition

## Slide 11: List of terms related to data acquisition
= Frame: One individual exposure of the detector (.edf image and 1D curve .dat)
= Measurement/Run: all frames for an individual acquisition (buffer or sample)
= DataCollection: combination of runs (buffer, sample, buffer)
In rare cases it could be (buffer, n*(buffer OR sample), buffer)
DataCollectionGroup : combined DataCollection for one macromolecule (minimum 3 concentrations). In a collection, by definition all samples are in the same buffer there is only one buffer measurement between samples which is classed as both the buffer_after in the first DC and the buffer_before in the subsequent DC.
Data collection Group for one macromolecule
…………………….
DC 1
DC 2
DC 3
DC n

## Slide 12: Visual Data Model Draft for Data Collection
………
Data Collection
Data Collection Group
Run
Frame
….
….
….
….
….
….
DataCollection
Run
Frame
Data Collection Array
Assembly
Macromolecule
Buffer + Sample + Buffer
Buffer or Sample

## Slide 14: Use Cases

## Slide 15: Case 1: How do the subunits fit together
An enzyme which in its functional form is comprised of 3 individual subunits (A, B and C). The first part of the Experiment ( P1) is to determine how the subunits fit together.
P1 will comprises data collections of:
- A, B and C individually
- The dimeric assemblyes of AB and BC
- The trimeric assembly ABC
Thus the assembly will have 6 individual macromolecules associated with it (A, B, C, AB, BC and ABC). Each with a minimum of 3 samples, all with the same buffer conditions
A*B*C*
A*C*
A*B*
C*
B*
A*
where n>=3
B1
Samples with different concentrations
Buffer
……………

## Slide 16: Case 1: How do the subunits fit together
ABC
AC
AB
C
B
A
All buffers for the same assembly should have the same conditions ? By default yes BUT they could change
B1
B1
…………..
B1
B1
…………..
B1
B1
…………..
B_AB
B_AB
…………..
B1
B1
…………..
B_ABC
B_ABC
…………..
Samples with different concentrations
Buffer 1

## Slide 17: Case 1: How do the subunits fit together
ABC
AC
AB
C
B
A
BUFFER + SAMPLE+ BUFFER
……..
Samples with different concentration (minimum 3)
Measurements
By definition is the same buffer
run
It could be in rare cases BUFFER + ….. + SAMPLE + SAMPLE + …. +BUFFER

## Slide 18: Case 1: How do the subunits fit together
ABC
AC
AB
C
B
A
Because there is only one buffer the datacollections overlap
……..
Data Collection Group
Measurements
DC
DC
DC
DC
DC
DC
DC
DC
DC
DC = DataCollection

## Slide 19: Case 1: How do the subunits fit together
ABC
AC
AB
C
B
A
Data collected with no optimization
Data Collection Array
……..
……..
……..
……..
Data Collection Group for A
Data Collection Group for B
Data Collection Group for C
Data Collection Group for AB
Data Collection Group for AC
Data Collection Group for ABC
……..
……..

## Slide 20: Case 1: How do the subunits fit together
Time Sequence Measurements
With No optimization
A
AC
C
B
AB
ABC
With optimization
A
AC
C
B
AB
ABC
Switching buffers with the same conditions in order to put them together
Data Collections are overlapping to avoid the extra buffer measurement
Problem is that we measure twice the same buffer
time

## Slide 21: Case 1: How do the subunits fit together
ABC
AC
AB
C
B
A
Data collected with buffer optimization
Data Collection Array
……..
……..
……..
……..
……..
……..
Data Collection Group for A
Data Collection Group for B
Data Collection Group for C
Data Collection Group for AB
Data Collection Group for AC
Data Collection Group for ABC
Because buffer for macromolecules A, B and C are the same no an extra buffer measurement is necessary between their data collections when measured sequentially

## Slide 22: Case 2: How does the enzyme function
P2 will comprises data collections of:
The trimeric assembly ABC (same conditions as for P1)
Plus a data collection for each buffer condition (Ligands and additives required for activity and /or non hydrolysable homologues to isolate the various stages of the reaction).
Thus the macromolecule ABC will have an additional n*3 samples where n is the number of buffer conditions that need to be measured.
ABC
AC
AB
C
B
A
……………
B1
Samples
Buffers Conditions c1
B2
Buffers Conditions c2
No measurements
ABC_B1_10_4C
ABC_B1_30_4C
ABC_B1_50_4C
ABC_B2_10_10C
ABC_B2_30_10C
ABC_B2_50_10C

## Slide 23: Case 2: How does the enzyme function
ABC
AC
AB
C
B
A
Measurements
…..
Buffer conditions 1
Buffer conditions 2
Buffer conditions 3

## Slide 24: Case 3: Kinetic
Designed to follow the reaction from start to finish (minutes or hours). In principle is one sample and by definition one condition, but the sample could be separate volumes from a large well and buffers could be measured as well
Time (t)
Reaction starts
Reaction ends
Reacting Sample
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Time between measurements
Total Time for measurements

## Slide 25: Case 3: Kinetic
If time between measurements > time for each measurement (buffer) then intersperse buffer measurements between samples.
Time (t)
Reaction starts
Reaction ends
Reacting Sample
Total Time for measurements
Frame
Frame
Frame
Frame
Frame
Frame
Buffer
Buffer
Buffer
Buffer
Buffer
Buffer
Frame
Frame
Frame
Frame
Frame
Frame
Frame
Buffer

## Slide 26: Sample Changer

## Slide 27: Plate Groups and Plates
Slot 1
Slot 2
Slot 3
Plate Group
Between 1 and 3 plates
Same storage temperature
It could contain different samples from different assemblies
Order the plates by something (ex. Temperature,
number of samples/buffer)?
Plate position

## Slide 28: Types of Plates
Attributes of the type:
Row count
Column count
Volume for each well
How can we fill the plate?
With samples and buffers associated to the same assembly
With samples and buffers coming from different assemblies
Only buffers
Only samples

## Slide 29
Session A (Static Wizard)
Experiment
AB
Buffer_A_10_1
A
A
A
Buffer_C_20_1
B
B
B
Buffer_AB_30_1
AB
AB
AB
Samples
Buffers
Plate Group (sample changer)
Assemblies
A
B
AB
Wizard:
How many macromolecules in ?
How many buffer conditions?
Define macromolecules / buffer?
Define the position
A
B
AB
AB
Plate Position

## Slide 30
Session B (Static Wizard)
Experiment AB
AB
Buffer_A_10_1
A
A
A
Buffer_C_20_1
B
B
B
Buffer_AB_30_1
AB
AB
AB
Samples
Buffers
Plate Group (sample changer)
Assemblies
A
B
AB
BC
Buffer_A_10_1
C
C
C
Buffer_B_20_1
B
B
B
Buffer_BC_30_1
BC
BC
BC
A
B
AB
Samples
Experiment AC
Static wizard allows just one assembly

## Slide 31
Session A
AB
Buffer_A_10_1
A
A
A
Buffer_C_20_1
B
B
B
Buffers
Plate Group (sample changer)
Assemblies
A
B
AB
Buffer_B_30_1
AB
AB
AB
Buffers
Plate Group (sample changer)
Assemblies
AB
Session B

## Slide 32: ISPYB – BsxCube Interface

## Slide 34: Robot
BsxCube
ISPyB
User logs in
Click on load robot from ISPyB
Reading actives sessions for user
findActiveSessionsByUserId
Return all actives sessions of this user
User chooses one
findPlateGroupsfromSessionId
Reading Plate groups of projects? associated to this sessionId
User chooses one
Reading all information about plateGroupId
findPlateGroupByPlateGroupId
Return all plate groups of this session
Return all plate group information
bsxCube fills the table

## Slide 35: Robot
BsxCube
ISPyB
Modifications
updateModification
Persist modifications
Collect the data
Store data collections
Persist data collections